MURRAY BRIDGE FLIGHT OFFICE

PALLAMANNA AIRFIELD

PIPER ARCHER II

WEIGHTS

Kgs                    lbs

Basic Empty weight  (inc full oil & unuseable fuel )      	695                    1528

Maximum take off weight   (normal )                                 	1159                  2550

# Maximum landing weight    (normal )                      		1159                  2550

Maximum take off weight   ( utility )                                  	968                    2130

Maximum Cabin Lift  With Full Tanks			335                    735

Maximum permissable baggage weight                             	90                      200

FUEL AND OIL                                                	Litres                 US/gall

Total Usable                                                                        	182                    48

Total  to tabs                                                                      	136                    35.8

Consumption rate / hr (planning)                                      	40                      10.6

Oil maximum                                                                      	7.6

Oil minimum                                                                       	6

AIRSPEEDS                                                      	Speed (kts)

Vne (never exceed)                                                            	154

Vno (max cruise)                                                                 	125

Va (max manoeuvring)                                                     	113

Vfe (max flap extension)                                                     	102

Vy (best rate of climb)                                                        	76

Vx (best angle of climb)                                                      	64

Vtoss (take off safety speed)                                             	59

Vs (nil flap)                                                                        	54

Vso (full flap)                                                                	47

Best glide                                                                             	76

TAS (flight planning)                                                         	120

Max crosswind component                                                 	17

APPROACH SPEEDS                                                    	kts

Base                                                                                       	80

Mid final                                                                                 75 - 70

At 50 feet                                                                                65

FLAP SETTINGS                                                            	Degrees

1st stage                                                                              	10

2nd stage                                                                             	25

3rd stage                                                                              	40

THESE ARE SUGGESTED FIGURES ONLY PLEASE REFER TO THE A/C FLIGHT MANUAL