MURRAY BRIDGE FLYING SCHOOL

PALLAMANNA AIRFIELD

PIPER WARRIOR  I

WEIGHTS  						                    Kgs                    lb

Empty aircraft      (inc full oil & unuseable fuel )                                 640                  1407

# Maximum take off weight   (normal )                                                 1055                  2325

Maximum landing weight    (normal )	       	                 	     1055	     2325

Maximum take off weight   ( utility )                                                    916                  2015

# Maximum landing weight    ( utility )                                                    916                  2015

Maximum permissable baggage weight                                                  90                    200

FUEL  AND OIL                                                                             Litres                US/gall

Total Usable                                                                                           181                47.6

Total  to tabs                                                                                          136                35.8

Consumption rate / hr (planning)                                                              35                 9.2

Oil maximum                                                                                             8

Oil minimum                                                                                              6

AIR SPEEDS                                                     		   Speed (knts)

## Vne (never exceed)                                             	 	        153

# Vno (max cruise)                                                                		        125

# Vma (max manoeuvring)                                                    	 	        111

# Vfe (max flap extension)                                                  		        102

# Vy (best rate of climb)                                                        	   	 	          75

# Vx (best angle)                                                                   		          65 (or as per ‘P chart)             Vtoss (take off safety speed)                                            		          67 (or as per ‘P chart)

# Vs (nil flap)                                                                       		          50

# Vso (full flap ext)                                                             	 	          44

# Best glide                                                                         	            75

# TAS (flight planning)                                                       		         105

# X-wind (max)                                                                   	            17

APPROACH                                                                   	                 Speed (knts)

# Base                                                                                	             80

# Mid final                                                                              	             75 > 70

# At 50 feet                                                                            	             65

FLAP SETTINGS                                                            	     Degrees

1st stage                                                                                   	            10

2nd stage                                                                                  	            25

3rd stage                                                                                   	            40

FULL FUEL		181 litres		131 kgs or 286 lbs

Available load		284 kgs or 632 lbs

Endurance		4 hrs 20 mins (plus reserves)

TAB FUEL		136 litres		98 kgs or 215 lbs

Available load		317 kgs or 703 lbs

Endurance		3 hrs 0 mins (plus reserves)

These are only recommended figures for accurate figures please consult poh & flight manual